## Slide 1: ASSESSMENT OF THE DISTRIBUTION OF THE PHYSIOCHEMICAL AND GEOCHEMICAL PROPERTIES IN RIVERS AND ESTUARIES: A CASE STUDY OF SOME PART OF ILAJE. PRESENTED BY OKOMOLEHIN, OLUWASEUN EMMANUEL MST/11/4673
Goals of study are to
• Determine and compare the water physiochemical parameters in the river and estuary.
• Determine the depths along the waterways to the ocean mouth.
• Determine and compare the concentration of heavy metals in the river and estuary sediment.
• Correlate result with standards and limits.

## Slide 2: The study area is the coastal region of Ondo State at the Ilaje Local Government area of the southwestern part of Nigeria between Lat. 5°50’ – 6° 20’N and Long. 4°40’ – 5° 05’ E.
The water surface physiochemical parameters at each sampling points were detected and recorded by the multi-meter probe and analyzer (HANNA HI 9828) directly in contact with the river and estuary, water depth was determined at each sampling point by the echo sounder (FURUNO LS-6100),and the Sediments from the bottom of river and estuary were obtained using the van veen grab, collected in polythene bags for laboratory heavy metal test.
Sediment samples collected were sun dried, grounded and sieved to grain size of < 200 µm. 1 grams of each sediments was measured and digested with volume of 5 ml mixture of 16 M HNO3 (J.T Baker) and 11.5 HCL (Fisher trace metal grade) in a ratio 2:1 into a conical flask, and whole mixture boiled at temperature of 150 °C and filtered with filter paper through funnel into a beaker. The metals obtained were regarded and analysed as pseudo-total metal because not all the silicate phase present in the sediments were dissolved but filtered out with an acid washed filters (45 µm pore size). The analyses of Fe, Pb, Cr, Zn and Cu in the digested samples were done using Flame Atomic Absorption Spectrometer (AAS) AA320N model with direct air-acetylene flame method.

## Slide 3
Chart: Sample location
| S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11 | S12 | S13 | S14 | S15 | S16 | S17 | S18 | S19 | S20 | S21 | S22 | S23 | S24
temp °C | 29.11 | 28.92 | 28.98 | 28.96 | 29.04 | 28.99 | 28.9 | 29.47 | 29.57 | 29.51 | 29.47 | 29.32 | 29.24 | 29.11 | 28.74 | 28.53 | 28.48 | 29.58 | 28.7 | 28.94 | 30.41 | 29.99 | 30.43 | 30.88
DO mg/l | 3.5 | 4.37 | 3.5 | 3.28 | 3.18 | 2.96 | 2.74 | 3.35 | 3.14 | 3.09 | 2.89 | 2.65 | 2.19 | 1.71 | 1.38 | 1.29 | 1.34 | 2.76 | 2.41 | 3.08 | 3.99 | 3.65 | 4.08 | 3.81
pH | 7.76 | 7.75 | 7.84 | 7.76 | 7.79 | 7.75 | 7.66 | 7.8 | 7.77 | 7.74 | 7.67 | 7.64 | 7.53 | 7.48 | 7.37 | 7.33 | 7.36 | 7.4 | 7.43 | 7.41 | 8.11 | 7.96 | 7.37 | 7.26
Chart: sample sites
| S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8 | S9 | S10 | S11 | S12 | S13 | S14 | S15 | S16
Zn mg/g | 21.9576 | 18.1048 | 21.4648 | 16.968 | 19.3032 | 17.2508 | 21.8456 | 19.8128 | 20.118 | 24.066 | 21.0476 | 21.3136 | 22.946 | 22.9264 | 21.6916 | 21.6916
Cu mg/g | 12.4768 | 8.4924 | 7.7504 | 7.0728 | 7.9968 | 2.6236 | 11.55 | 7.6272 | 1.7276 | 10.1892 | 9.6656 | 9.8196 | 12.9696 | 10.4384 | 10.962 | 9.1084
Pb mg/g | 27.3056 | 72.814 | 60.3008 | 34.132 | 48.9216 | 71.6772 | 47.7848 | 32.9952 | 80.78 | 44.3716 | 75.0904 | 67.1272 | 125.1516 | 91.0196 | 63.714 | 120.5988
Lead, zinc and copper concentration in different locations.
Salinity, temperature and density variation
Temperature, DO and pH variation across sample locations

## Slide 4
The temperature of all the locations is generally high with the temperature highest at Station 24 having a value of 30.88°C and lowest at Station 17 having a value of 28.48°C. Though the observed temperatures fall within the acceptable limits for aquatic lives, 20°C–33°C, however, such high records are capable of reducing the dissolved oxygen, which is another important factor influencing aquatic lives. Temperature controls the solubility of gases in water, and the reaction rate of chemicals.
From the estuary through the rivers the pH is majorly around 7 except for Station 21 which has a pH of 8.11, thus the pH ranges between 7.26 and 8.11. The mean pH values were well within the acceptable range for drinking water (6.5 to 8.5), optimal aquatic productivity (6.5 to 9.0), and a livable range of 5.5 to 10 (Wetzel 2001).
The amount of dissolved oxygen in the river is averagely higher than the amount in the estuary though the highest value of dissolved oxygen 4.37 mg/l was obtained in the estuary at Station 2 and the lowest in the river at Station 16 with a recorded value of 1.29 mg/l. The amount of DO is generally too low in the water body, concentrations of DO above 5 mg/L are considered supportive of marine life, while concentrations below this are potentially harmful.
Lead ranges from 27.3056 mg/g at Station 1 to 125.1516 mg/g at Station 13, Pb is averagely higher than USEPA standard which is 40 mg/g. Pb concentration is high in some location, even at lower doses, it can cause anemia and kidney damage. Pb is introduced into this environments through fuel exhaust from boat, batteries, and paint pigment.
Zinc ranges from. 16.968 mg/g at Station 4 to 22.946 mg/g at Station 13. It is evenly spread across the sample location from estuary to river and its concentration is displayed in an unpolluted degree compared with standard. Copper ranges from 1.7276 mg/g at Station 9 to 12.9696 mg/g at Station 13. Copper just like Zn displays its concentration in an unpolluted degree. Major anthropogenic sources of Cu include agrochemicals (fertilizers and pesticides), wood preservatives, electroplating, and antifouling paints.
Salinity, temperature and density data were plotted into a graph to show how water is driven by density and how saline and fresh water are mixed, the colder water with high salinity are the densest water, though salinity play more role in the stratification of the water, temperature also contributes to the water mass. In the region around temperature of 29.5°C and salinity between 15 and 30 the graph forms an antiform showing how serious mixing between the fresh and saline water is going on there
Source: EPA 2012.
Source: WHO (1996, 2004, 2006, 2011) and USEPA

## Slide 5: SUMMARY
Aspects of the physicochemical parameters of Abereke estuary and rivers was investigated in a period of a single day, to assess the physicochemical chemical parameter a multimeter-probe was used to take a measurement of temperature, salinity, density, TDS, pressure, pH, DO, conductivity along the waterways. The physicochemical behaviour was described to see the spatial variation to evaluate the interaction between the river and the estuary.
Heavy metals in sediments were also evaluated, Sediment samples were collected at some locations within the stretch of the exploration, to be able to visualize how copious heavy metals are in the estuary and rivers, and how human activities such as agricultural practice and transportation affect the concentration of heavy metal in various location.